To Do:
1. DMA system description
  1. unless a secondary master requires a command to initiate a bus request, it must include logic to wait for other transfers to conclude before requesting
  2. PM must wait and hold ack until brq is deasserted
    1. cutting the SM off mid-transaction will lead to corrupt memory.
2. Timing diagrams for some signals
  1. Read Operation
  2. Write Operation
  3. Separate WAIT timing diagram?
  4. Card Select
    1. Does this provide any more information than a standard read/write diagram?
  5. Memory Inhibit
    1. What is there to explain? Is it already covered by specifying it in the read/write diagrams?
  6. bus arbitration
  7. Should specify minimum setup/hold, various timings.
  8. Should timings be pretty loose?
  9. Timing is pretty key
    1. Read cycle – IOSEL, CSX, A19..0 all need to remain stable until well after RD or WR is deasserted. Need hold time. Data bus drivers also need to remain active for this time.
    2. RD and WR need to be asserted later than IOSEL, CSX, A19..0 are stable.
    3. Need to consider propagation delay of all drivers and decoders in the path of group A signals.
    4. Specify timings for slave cards, that masters must then allow for?
    5. Slave should take data on rising edge of WR.
    6. Does master need to ensure data is valid before WR is asserted?
  10. Note that RD and WR may not be asserted simultaneously

1. Discuss address space layouts
  1. Acknowledge the fact that different architectures have different layouts
  2. Primary master defines memory map and must document it.
2. Card-specific signals and implementations
  1. CSX
  2. IRQX
  3. V<7..0>
3. Implementations
  1. Address lines
    1. Masters required to drive all 20 address lines tri-state (This is implied already but could be added to 2.1.1.)
4. 2.1.8 – recommend slow (or any) devices assert WAIT? Refer to other part of the document where this is mentioed?
5. Recommend a termination circuit?