To Do:
1. DMA system description
  1. unless a secondary master requires a command to initiate a bus request, it must include logic to wait for other transfers to conclude before requesting
  2. PM must wait and hold ack until brq is deasserted
    1. cutting the SM off mid-transaction will lead to corrupt memory.
2. Timing diagrams for some signals
  1. Card Select
    1. Does this provide any more information than a standard read/write diagram?
  2. Memory Inhibit
    1. What is there to explain?
  3. Need to review timing parameters on real hardware
3. Card-specific signals and implementations
  1. CSX
  2. IRQX
  3. V<7..0>
4. Implementations
  1. Address lines
    1. Masters required to drive all 20 address lines tri-state (This is implied already but could be added to 2.1.1.)
5. Consider renaming INTS to SINT
6. Consider replacing NC pins with distributed 0V pins (approximately either side of A<19..0>)