To Do:
1. DMA system description
  1. unless a secondary master requires a command to initiate a bus request, it must include logic to wait for other transfers to conclude before requesting
  2. PM must wait and hold ack until brq is deasserted
    1. cutting the SM off mid-transaction will lead to corrupt memory.
2. Timing diagrams for some signals
  1. Read Operation
  2. Write Operation
  3. Card Select
  4. Memory Inhibit
  5. bus arbitration
  6. Should specify minimum setup/hold, various timings.
  7. Timings should be pretty loose
3. Define I/O space
  1. Backplane onboard peripherals – should be assigned a slot number – either above all other slots or selectable to take the place of a physical slot.
4. Discuss address space layouts
  1. Acknowledge the fact that different architectures have different layouts
  2. Primary master defines memory map and must document it.
5. Card-specific signals and implementations
  1. CSX
  2. IRQX
  3. V0-7
6. Primary master implementation
  1. Address lines
    1. Required to drive all 20 address lines (tri-state)
  2. Interrupt implementation
    1. vectoring not required
7. Interrupts
  1. If a prioritization mechanism exists, priority must be given to lower IRQs first
  2. Differences between signals
8. Electrical Specifications
9. Technical drawings
  1. Card specifications
    1. Specify clearance from mounting holes that must be isolated