To Do:
1. DMA system description
  1. unless a secondary master requires a command to initiate a bus request, it must include logic to wait for other transfers to conclude before requesting
  2. PM must wait and hold ack until brq is deasserted
    1. cutting the SM off mid-transaction will lead to corrupt memory.
2. Timing diagrams for some signals
  1. Read Operation
  2. Write Operation
  3. Card Select
  4. Memory Inhibit
  5. bus arbitration
  6. Should specify minimum setup/hold, various timings.
  7. Timings should be pretty loose
3. Define I/O space
  1. Backplane onboard peripherals – should be assigned a slot number – either above all other slots or selectable to take the place of a physical slot.
4. Discuss address space layouts
  1. Acknowledge the fact that different architectures have different layouts
  2. Primary master defines memory map and must document it.
5. Card-specific signals and implementations
  1. CSX
  2. IRQX
  3. IRQ0-7
6. Primary master implementation
  1. Address lines
    1. Required to drive all 20 address lines
  2. Interrupt implementation
    1. vectoring not required
7. Interrupts
  1. If a prioritization mechanism exists, priority must be given to lower IRQs first
  2. Differences between signals
    1. Interrupt means it will interrupt the CPU directly?
      1. That kind of makes it implementation-dependent
      2. Should INT be renamed to something less confusing?
    2. Interrupt Request means it will request an interrupt from the handler circuit and get one if/when appropriate.
    3. Unvectored interrupt used by backplane (should have its own interrupt register/priority encoder for irqs above slot 7.
  3. Vectoring is not required, can OR the IRQ lines to sum them logically
  4. Summing interrupt signals together for a simple logical-OR requires consideration of the pull-up loading.
    1. 10 interrupt signals summed together, each with two 270Ω terminations to 2.7V is equivalent to 13.5Ω.
8. Electrical Specifications
9. Technical drawings
  1. Card specifications
    1. Specify clearance from mounting holes that must be isolated