To Do:
1. DMA system description
  1. unless a secondary master requires a command to initiate a bus request, it must include logic to wait for other transfers to conclude before requesting
  2. PM must wait and hold ack until brq is deasserted
    1. cutting the SM off mid-transaction will lead to corrupt memory.
2. Timing diagrams for some signals
  1. Read Operation
  2. Write Operation
  3. Card Select
  4. Memory Inhibit
  5. bus arbitration
  6. Should specify minimum setup/hold, various timings.
  7. Timings should be pretty loose
3. Discuss address space layouts
  1. Acknowledge the fact that different architectures have different layouts
  2. Primary master defines memory map and must document it.
4. Card-specific signals and implementations
  1. CSX
  2. IRQX
  3. V<7..0>
5. Implementations
  1. Address lines
    1. Masters required to drive all 20 address lines tri-state (This is implied already but could be added to 2.1.1.)
6. 2.1.8 – recommend slow (or any) devices assert WAIT? Refer to other part of the document where this is mentioed?
7. Recommend a termination circuit?