# General Description
The XMICRO-LPA is an XMICRO development tool which breaks out all bus signals into high-density connectors compatible with HP/Agilent logic analyzers.
## Features
- For use with HP/Agilent E5346A High Density Probe Adapter
- Minimal skew on critical signals
## System Outline
Signal Length (mm) Total Delay (ps) Skew (ps) / D5 66.42 380.80 -7.74 / D6 66.69 382.35 -6.19 / D7 66.79 382.92 -5.62 / D2 66.90 383.55 -4.99 / V7 67.04 384.36 -4.19 / A11 67.13 384.87 -3.67 / D3 67.17 385.10 -3.44 / A14 67.18 385.16 -3.38 / D4 67.21 385.33 -3.21 / A13 67.29 385.79 -2.75 / A5 67.29 385.79 -2.75 / A15 67.29 385.79 -2.75 / A1 67.38 386.30 -2.24 / A6 67.40 386.42 -2.12 / A10 67.40 386.42 -2.12 / D0 67.43 386.59 -1.95 / A2 67.49 386.94 -1.61 / A9 67.51 387.05 -1.49 / A7 67.51 387.05 -1.49 / A4 67.55 387.28 -1.26 / A12 67.55 387.28 -1.26 / A0 67.58 387.45 -1.09 / D1 67.65 387.85 -0.69 / A3 67.66 387.91 -0.63 / NMI 67.77 388.54 0.00	Signal Length (mm) Total Delay (ps) Skew (ps) / RD 67.77 388.54 0.00 / WR 67.77 388.54 0.00 / A8 67.77 388.54 0.00 / A18 67.89 389.23 0.69 / A19 68.03 390.03 1.49 / V6 68.42 392.27 3.73 / A17 68.56 393.07 4.53 / A16 68.70 393.87 5.33 / INH 69.52 398.57 10.03 / V5 70.85 406.20 17.66 / WAIT 71.57 410.33 21.79 / V4 72.23 414.11 25.57 / IOSEL 72.54 415.89 27.35 / FETCH 74.38 426.44 37.90 / V3 74.66 428.04 39.50 / V2 76.04 435.95 47.41 / V1 78.47 449.89 61.35 / V0 79.85 457.80 69.26 / SINT 81.23 465.71 77.17 / CLK 87.07 499.19 110.65 / HALT 90.02 516.10 127.56 / BUSAK 93.51 536.11 147.57 / BUSRQ 94.89 544.03 155.48 / CSX 97.32 557.96 169.42 / RST 98.70 565.87 177.33