To Do:
1. Table of Contents
2. DMA system description
  1. unless a secondary master requires a command to initiate a bus request, it must include logic to wait for other transfers to finish before requesting
  2. must also tristate if the busack signal is deasserted.
3. Table of signal directions for both masters and slaves
4. Timing diagrams for most/all signals
  1. Read Operation
  2. Write Operation
  3. Card Select
  4. Memory Inhibit
5. Define I/O space
  1. 256 bytes per card
  2. Specific implementation required or recommended?
    1. Probably should be required
    2. Could cause serious software incompatibility between backplanes if not required
  3. Backplane onboard peripheral addresses – should be assigned a slot number - Next above the top slot.
6. Discuss address space layouts
  1. Acknowledge the fact that different architectures have different layouts
  2. Primary master defines memory map and must document it.
  3. RAM, ROM, I/O
  4. Extended memory overridden by cards
    1. Recommend to use an address comparator to be able to adjust for differnt architectures
7. Card-specific signals and implementations
  1. CSX
  2. IRQX
  3. IRQ0-7
8. Primary master implementation
  1. Address lines
    1. Required to drive all 20 address lines
  2. Interrupt implementation
9. Interrupts
  1. Differences between signals
    1. Interrupt means it will interrupt the CPU directly
    2. Interrupt Request means it will request an interrupt from the handler circuit and get one if/when appropriate.
    3. Unvectored interrupt used by backplane (should have its own interrupt register/priority encoder for irqs above slot 7.
10. Electrical Specifications