To Do:
1. DMA system description
  1. unless a secondary master requires a command to initiate a bus request, it must include logic to wait for other transfers to finish before requesting
  2. must also tristate if the busack signal is deasserted?
  3. Maybe the PM should be required to wait until brq is deasserted
    1. cutting the SM off mid-transaction will lead to corrupt memory.
2. Timing diagrams for some signals
  1. Read Operation
  2. Write Operation
  3. Card Select
  4. Memory Inhibit
  5. bus arbitration
  6. Should specify minimum setup/hold, various timings.
  7. Timings should be pretty loose
3. Define I/O space
  1. Specific implementation required or recommended?
    1. Probably should be required
    2. Could cause serious software incompatibility between backplanes if not required
  2. Backplane onboard peripherals – should be assigned a slot number – Preferably selectable
  3. Large backplane interrupt vector – reserved byte
4. Discuss address space layouts
  1. Acknowledge the fact that different architectures have different layouts
  2. Primary master defines memory map and must document it.
  3. RAM, ROM, I/O
  4. Extended memory overridden by cards
    1. Recommend to use an address comparator to be able to adjust for different architectures
5. Card-specific signals and implementations
  1. CSX
  2. IRQX
  3. IRQ0-7
6. Primary master implementation
  1. Address lines
    1. Required to drive all 20 address lines
  2. Interrupt implementation
7. Interrupts
  1. Differences between signals
    1. Interrupt means it will interrupt the CPU directly
    2. Interrupt Request means it will request an interrupt from the handler circuit and get one if/when appropriate.
    3. Unvectored interrupt used by backplane (should have its own interrupt register/priority encoder for irqs above slot 7.
  2. Change vectored interrupt scheme?
    1. IRQ<7..0> become a priority (drop some of them)
      1. IRQX generates an encoded priority on the backplane, IRQ is asserted.
        1. Prioritized interrupt can be decoded by the PM or used as a vector
      2. Some things would become more difficult
        1. Masking interrupts
        2. routing IRQX signals on the backplane
        3. Using special interrupt chips like intel’s would require decoding
        4. Masking interrupts would block any lower priority interrupts.
    2. INT becomes a “high interrupt” bit (IRQ<7..0> become IRQ<15..8>)
      1. INT alone is still un-vectored
      2. could possibly use diodes to assert INT and IRQ<7..0> using IRQX<15..8>
      3. In this case, if INT is asserted, no way to tell that a higher priority IRQ (low interrupt) is not active.
8. Electrical Specifications
9. Technical drawings
  1. Card specifications
    1. Specify clearance from mounting holes that must be isolated
    2. Rewrite or remove notes on drawings.